## Slide 1: More about electromagnets

## Slide 2: The Magnetic Field Around a Current Carrying Wire.
The field is concentric circles.
The direction is given by the right hand grip rule.

## Slide 3: How can electricity make a magnet?
When a current passes through the coil it acts like a magnet – there is a magnetic field around it.
If you put a magnetic material such as an iron nail into the centre or core of the solenoid, the magnetic field gets even stronger.
You have made a magnet using electricity – we call it an electromagnet.

## Slide 4: The Magnetic Field Around a Solenoid

## Slide 5: Electromagnetism in action
Keywords:
Switch
Relay
Electromagnet
Attraction
What are the advantages of an electromagnet over a permanent magnet?
Name three devices that make use of induced (electro) magnets.
How could we make this electromagnet stronger?

## Slide 6: The Electric Bell

## Slide 8: A Relay Circuit
When you turn an electric shower on, you switch on a low-current circuit.
An electromagnet moves a switch called a relay, and this turns on another much more powerful circuit which powers the water heater and pump.
So you switch on a low-current circuit, which in turn switches on a high-current circuit.
This is safer than switching on the powerful circuit directly.

## Slide 9
Using your knowledge of electromagnets, explain how this door lock works.

## Slide 10: Magnetic flux density
What do each of the letters represent?
F = Force (N)
B =
I =
L =
If a wire is in a flux density of 0.05T, a current flowing of 25A and is 3m long, what would the force be on that wire?
How would you rearrange the equation to calculate current flowing?