## Slide 1
Mechanics
Applications of Forces
Twitter: @Owen134866
www.mathsfreeresourcelibrary.com

## Slide 2: Prior knowledge check
1) A particle of mass 2kg sits on a rough plane that is inclined at 45˚ to the horizontal. A force of 10N acts on the particle up the slope, parallel to the plane. Given that the particle is in limiting equilibrium, calculate the coefficient of friction, .
2) A uniform rod of length 2m and mass 5kg rests in equilibrium at an angle of 60˚ to the horizontal. The rod is pivoted at and a force of magnitude acts perpendicular to the rod at . Find the value of .
60˚
0.278
12.3N

## Slide 3
Teachings for Exercise 7A

## Slide 4: Applications of Forces
7A
A particle is in static equilibrium if it is at rest and the resultant forces acting on it are equal to 0.
This is in contrast to dynamics, where a particle is being caused to move in some way by combinations of forces…
You need to be able to solve problems involving static particles

## Slide 5: Applications of Forces
You need to be able to solve problems involving static particles
You should:
Draw a diagram and label the forces
Resolve into horizontal/vertical or parallel/perpendicular components
Set the sums equal to 0 (as the objects are in equilibrium, the forces acting in opposite directions must cancel out…
Solve the equations to find the unknown forces…
y
x
4N
P N
Q N
30°
45°
4Sin45
4Cos45
PCos30
PSin30
The particle to the left is in equilibrium. Calculate the magnitude of the forces P and Q.
 This means the horizontal and vertical forces cancel out (acceleration = 0 in both directions so F = 0)
Choose a direction as positive and sub in values
Rearrange
Divide by Cos30
Resolve Horizontally
Calculate
7A

## Slide 6: Applications of Forces
You need to be able to solve problems involving static particles
You should:
Draw a diagram and label the forces
Resolve into horizontal/vertical or parallel/perpendicular components
Set the sums equal to 0 (as the objects are in equilibrium, the forces acting in opposite directions must cancel out…
Solve the equations to find the unknown forces…
y
x
4N
P N
Q N
30°
45°
4Sin45
4Cos45
PCos30
PSin30
The particle to the left is in equilibrium. Calculate the magnitude of the forces P and Q.
 This means the horizontal and vertical forces cancel out (acceleration = 0 in both directions so F = 0)
Choose a direction as positive and sub in values
Add Q
Calculate Q using the exact value of P from the first part
Resolve Vertically
P = 3.27N
You will usually need to identify which direction is solvable first, then solve the second direction after!
7A

## Slide 7: Applications of Forces
You need to be able to solve problems involving static particles
The diagram to the right shows a particle in equilibrium under a number of forces.
Calculate the magnitudes of the forces P and Q
 Start by resolving in both directions
y
x
Q N
P N
1N
2N
40°
55°
PSin40
QSin55
QCos55
PCos40
Choose a direction as positive and sub in values
Resolve Horizontally
Choose a direction as positive and sub in values
Resolve Vertically
Simplify
1)
2)
7A

## Slide 8: Applications of Forces
You need to be able to solve problems involving static particles
The diagram to the right shows a particle in equilibrium under a number of forces.
Calculate the magnitudes of the forces P and Q
 Start by resolving in both directions
You can now solve these by rearranging one and subbing it into the other!
Q = 0.769N
y
x
Q N
P N
1N
2N
40°
55°
PSin40
QSin55
QCos55
PCos40
2)
Replace P with the Q equivalent
Multiply all terms by Cos40
Add Cos40
Factorise Q on the left side
Divide by the bracket
Calculate
1)
2)
7A

## Slide 9: Applications of Forces
You need to be able to solve problems involving static particles
The diagram to the right shows a particle in equilibrium under a number of forces.
Calculate the magnitudes of the forces P and Q
 Start by resolving in both directions
You can now solve these by rearranging one and subbing it into the other!
Q = 0.769N
P = 0.576N
y
x
Q N
P N
1N
2N
40°
55°
PSin40
QSin55
QCos55
PCos40
1)
Sub in Q (use the exact value)
Calculate
1)
2)
7A

## Slide 10: Applications of Forces
You need to be able to solve problems involving static particles
The diagram shows a particle in equilibrium on an inclined plane under the effect of the forces shown.
Find the size of angle θ and the value of force P.
 Start by splitting forces into parallel and perpendicular directions
2N
PN
8N
5N
θ
30°
30°
PCosθ
PSinθ
5Cos30
5Sin30
Resolving Parallel
Resolving Perpendicular
1)
2)
Use P as the positive direction and sub in values
Rearrange to leave PCosθ
Use P as the positive direction and sub in values
Rearrange to leave PSinθ
7A

## Slide 11: Applications of Forces
You need to be able to solve problems involving static particles
The diagram shows a particle in equilibrium on an inclined plane under the effect of the forces shown.
Find the size of angle θ and the value of force P.
 Start by splitting forces into parallel and perpendicular directions
2N
PN
8N
5N
θ
30°
PCosθ
PSinθ
5Cos30
5Sin30
1)
2)
1)
2)
Divide equation 2 by equation 1
Each side must be divided as a whole, not individual parts
P’s cancel, Sin/Cos = Tan
Work out the fraction
Use inverse Tan
7A
30°

## Slide 12: Applications of Forces
You need to be able to solve problems involving static particles
The diagram shows a particle in equilibrium on an inclined plane under the effect of the forces shown.
Find the size of angle θ and the value of force P.
 Start by splitting forces into parallel and perpendicular directions
2N
PN
8N
5N
θ
30°
PCosθ
PSinθ
5Cos30
5Sin30
1)
2)
1)
Divide by Cosθ
Sub in the exact value for θ
Calculate P
7A
30°

## Slide 13
Teachings for Exercise 7B

## Slide 14: Section 7B Modelling with statics
You need to know when to include additional forces on your diagrams, such as
weight, tension, thrust, the normal reaction and friction

## Slide 15: Applications of Forces
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A smooth bead, Y, is threaded on a light inextensible string. The ends of the string are attached to two fixed points X and Z on the same horizontal level. The bead is held in equilibrium by a horizontal force of 8N acting in the direction ZX. Bead Y hangs vertically below X and angle XZY = 30°.
Find:
The tension in the string
The weight of the bead
X
Z
Y
30°
mg
8
30°
T
T
Draw a diagram
Since this is only one string and it is inextensible, the tension in it will be the same
Call the mass m, since we do not know it…
TCos30
TSin30
Resolve Horizontally
Sub in values, choosing T as the positive direction
Add 8
Divide by Cos30
Calculate
7B

## Slide 16: Applications of Forces
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A smooth bead, Y, is threaded on a light inextensible string. The ends of the string are attached to two fixed points X and Z on the same horizontal level. The bead is held in equilibrium by a horizontal force of 8N acting in the direction ZX. Bead Y hangs vertically below X and angle XZY = 30°.
Find:
The tension in the string
The weight of the bead
X
Z
Y
30°
mg
8
30°
T
T
Draw a diagram
Since this is only one string and it is inextensible, the tension in it will be the same
Call the mass m, since we do not know it…
TCos30
TSin30
Resolve Vertically
Sub in values, choosing T as the positive direction
Add mg
Sub in the value of T
This is all we need!
The question asked for the weight, not the mass! (weight being mass x gravity…)
Be careful on this type of question. If particle is held by 2 different strings, the tensions may be different in each!
7B

## Slide 17: Applications of Forces
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A mass of 3kg rests on the surface of a smooth plane inclined at an angle of 45° to the horizontal. The mass is attached to a cable which passes up the plane and passes over a smooth pulley at the top. The cable carries a mass of 1kg which hangs freely at the other end. There is a force of PN acting horizontally on the 3kg mass and the system is in equilibrium.
By modelling the cable as a light inextensible string and the masses as particles, calculate:
The magnitude of P
The normal reaction between the mass and the plane
45˚
45˚
45˚
R
T
T
1g
3g
3gCos45
3gSin45
PCos45
P
PSin45
Find the tension using the 1kg mass
Resolve in the direction of T and sub in values
Add 1g
9.8N
9.8N
7B

## Slide 18: Applications of Forces
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A mass of 3kg rests on the surface of a smooth plane inclined at an angle of 45° to the horizontal. The mass is attached to a cable which passes up the plane and passes over a smooth pulley at the top. The cable carries a mass of 1kg which hangs freely at the other end. There is a force of PN acting horizontally on the 3kg mass and the system is in equilibrium.
By modelling the cable as a light inextensible string and the masses as particles, calculate:
The magnitude of P
The normal reaction between the mass and the plane
45˚
45˚
45˚
R
1g
3g
3gCos45
3gSin45
PCos45
P
PSin45
Resolve Parallel to find P
9.8N
9.8N
Choose P as the positive direction and sub in values
Rearrange
Divide by Cos45
Calculate
7B

## Slide 19: Applications of Forces
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A mass of 3kg rests on the surface of a smooth plane inclined at an angle of 45° to the horizontal. The mass is attached to a cable which passes up the plane and passes over a smooth pulley at the top. The cable carries a mass of 1kg which hangs freely at the other end. There is a force of PN acting horizontally on the 3kg mass and the system is in equilibrium.
By modelling the cable as a light inextensible string and the masses as particles, calculate:
The magnitude of P
The normal reaction between the mass and the plane
45˚
45˚
45˚
R
1g
3g
3gCos45
3gSin45
PCos45
P
PSin45
Resolve Perpendicular to find R
9.8N
9.8N
Choose R as the positive direction and sub in values
Rearrange
Calculate
7B
Note that in this question we used the modelling assumption that the pulley is smooth (this would cause the tension to be equal either side

## Slide 20
Teachings for Exercise 7C

## Slide 21: Section C Friction and Static Particles
We have seen before that FMAX is the maximum frictional force possible between two surfaces, and that it will resist any force up to this amount
Remember that the frictional force can be lower than this and still prevent movement
In statics, FMAX is reached when a body is in limiting equilibrium, i.e.) on the point of moving
It is important to consider which direction the object is about to move as this affects the direction the friction is acting…
You can also solve statics problems by using the relationship

## Slide 22: Applications of Forces
You can also solve statics problems by using the relationship
We have seen before that FMAX is the maximum frictional force possible between two surfaces, and that it will resist any force up to this amount
Remember that the frictional force can be lower than this and still prevent movement
In statics, FMAX is reached when a body is in limiting equilibrium, ie) on the point of moving
It is important to consider which direction the object is about to move as this affects the direction the friction is acting…
A block of mass 3kg rests on a rough horizontal plane. The coefficient of friction between the block and the plane is 0.4. When a horizontal force P N is applied to the block, the block remains in equilibrium.
Find the value for P for which the equilibrium is limiting
Find the value of F when P = 8N
R
3g
3kg
P
F
Resolve vertically for R
Sub in values with R as positive
Add 3g
Find FMAX
Sub in values
Calculate
For part b), if P = 8N then equilibrium is not limiting, and P will be matched by a frictional force of 8N
3g
So if P = 11.76N, then the block is in limiting equilibrium on the point of moving
7C

## Slide 23: Applications of Forces
You can also solve statics problems by using the relationship
A mass of 8kg rests on a rough horizontal plane. The mass may be modelled as a particle, and the coefficient of friction between the mass and the plane is 0.5.
Find the magnitude of the maximum force PN, which acts on this mass without causing it to move if P acts at an angle of 60° above the horizontal.
8g
8kg
P
F
R
60°
PCos60
PSin60
Draw a diagram
 Find the normal reaction as we need this for FMAX
Resolve Vertically
Find FMAX
Sub in values with R as positive
Rearrange to find R in terms of P
Sub in values
Multiply bracket out
7C

## Slide 24: Applications of Forces
You can also solve statics problems by using the relationship
A mass of 8kg rests on a rough horizontal plane. The mass may be modelled as a particle, and the coefficient of friction between the mass and the plane is 0.5.
Find the magnitude of the maximum force PN, which acts on this mass without causing it to move if P acts at an angle of 60° above the horizontal.
8g
8kg
P
F
R
60°
PCos60
PSin60
Draw a diagram
 Find the normal reaction as we need this for FMAX
Resolve Horizontally
Sub in values with P as positive
 The horizontal forces will cancel out as the block is in limiting equilibrium
Sub in FMAX
‘Multiply out’ the bracket
Add 4g
Factorise P on the left side
Divide by the bracket
Calculate
If is any greater, the block will start to accelerate.
If is any smaller, then FMAX will be less and hence the block will not be in limiting equilibrium
7C

## Slide 25: Applications of Forces
You can also solve statics problems by using the relationship
A box of mass 10kg rests in limiting equilibrium on a rough plane inclined at 20° above the horizontal. Find the coefficient of friction between the box and the plane.
Draw a diagram
We need to find FMAX so begin by calculating the normal reaction
20
20
10g
10gCos20
10gSin20
R
F
Resolving Perpendicular
Finding FMAX
Sub in values with R as positive
Rearrange
Sub in R and leave µ
7C

## Slide 26: Applications of Forces
You can also solve statics problems by using the relationship
A box of mass 10kg rests in limiting equilibrium on a rough plane inclined at 20° above the horizontal. Find the coefficient of friction between the box and the plane.
Draw a diagram
We need to find FMAX so begin by calculating the normal reaction
Now you can resolve Parallel to find
20
20
10g
10gCos20
10gSin20
R
F
Resolving Parallel
Sub in values with ‘down the plane’ as positive
Sub in FMAX
Add µ(10gCos20)
Divide by the bracket
Calculate
7C

## Slide 27: Applications of Forces
You can also solve statics problems by using the relationship
A horizontal force of magnitude is applied to the box. Given that the box remains in equilibrium, find the maximum value of .
It is very important to notice that this force will be attempting to push the box up the slope
Hence, the direction of the frictional force will change…
As before, find the normal reaction, and use it to find the maximum frictional force
Then resolve parallel using this value…
20
20
10g
10gCos20
10gSin20
R
F
7C
20˚
PCos20
P
PSin20
Resolving Perpendicular
Sub in values with R as positive
Rearrange
Finding FMAX
Sub in R (we can leave as it is for now to avoid rounding errors…)
Now update the diagram with this information…

## Slide 28: Applications of Forces
You can also solve statics problems by using the relationship
A horizontal force of magnitude is applied to the box. Given that the box remains in equilibrium, find the maximum value of .
It is very important to notice that this force will be attempting to push the box up the slope
Hence, the direction of the frictional force will change…
As before, find the normal reaction, and use it to find the maximum frictional force
Then resolve parallel using this value…
20
20
10g
10gCos20
10gSin20
R
7C
20˚
PCos20
P
PSin20
Resolving Parallel
Sub in values with ‘up the plane’ as positive
Expand bracket
Rearrange
Factorise left side
Divide by bracket
Calculate using the exact value of

## Slide 29
Teachings for Exercise 7D

## Slide 30: STARTER
Question 1: A uniform rod AB of length 6 m and mass 5 kg is resting on a smooth pivot 1 m from A. It is held in equilibrium by means of a light inextensible string attached to the rod 5 m from A. The other end of the string is fixed to a point vertically above A so that the angle it makes with the rod is 30°.
Find the tension in the string if the rod is in equilibrium.
5g × 2 = T sin 30° × 4
T = 5g
10g = 2T
T
A
B
5g
1
1
2
2
30
R
T sin 30°
Take moments about the pivot:
T = 49 N
Notes: The tension in the string has been resolved. Its component perpendicular to the body is Tsin.

## Slide 31: Equilibrium and rigid bodies
Rods are sometimes said to be freely hinged or smoothly hinged. In this case there will be a reaction at the hinge but the direction of this reaction is not known. Hence horizontal and vertical components of the reaction force are used in the solution.
A rigid body is one that does not bend or change shape when forces are applied to it. Possible examples are rods and ladders.
For a rigid body to be in equilibrium two conditions need to be satisfied:
The vector sum of the forces acting on the body must be zero.
The sum of the moments about any point must be zero.

## Slide 32: Equilibrium and rigid bodies
B
70
A
Since the ladder is uniform, the weight will act through its mid-point.
Question 1: A uniform ladder of length 4 m and weight 6 kg rests on rough horizontal ground against a smooth vertical wall. The ladder is inclined at an angle of 70° to the vertical when it is on the point of slipping. Calculate the coefficient of friction between the ladder and the ground.
S
6g
2
2
We first need to draw a diagram showing the forces acting on the ladder.
R
F
There is a normal contact force from the smooth wall.
The total reaction force on the ladder from the rough ground has normal and frictional components, R and F.

## Slide 33: Use the solution from the textbook!!
Resolving vertically gives: R = 6g
Take moments about A: (6g cos 70° × 2) = (S sin 70° × 4)
(F = S and R = 6g:) 3g cot 70° = 6µg
B
70
A
S
6g
2
2
R
F
Resolving horizontally gives: F = S
S sin 70°
6g cos 70°
In order to take moments we need to use the components of S and 6g perpendicular to the ladder.
S =
= 3g cot 70°
The ladder is on the point of slipping, so F = µR.
 µ = ½ cot 70°
= 0.182 (3 s.f.)

## Slide 34: Applications of Forces
15°
40gSin15
You can solve problems about rigid bodies resting in limiting equilibrium
If a body is on the point of moving it is said to be in limiting equilibrium. In this case, the frictional force takes its maximum value, µR, where µ is the coefficient of friction and R is the normal reaction.
A uniform rod AB of mass 40kg and length 10m rests with the end A on rough horizontal ground. The rod rests against a smooth peg C where AC = 8m. The rod is in limiting equilibrium at an angle of 15° to the horizontal. Find:
The magnitude of the reaction at C
The coefficient of friction between the rod and the ground
15°
40g
40gCos15
R
F
N
5m
3m
2m
Draw a diagram and label all the forces: Weight, the normal reactions and friction. Split into components if needed
The rod will have a tendency to slide downwards, with the base moving to the left. Hence, friction will oppose this
Taking moments about A will mean we can find the normal reaction at the peg.
Taking moments about A
(1)
(2)
(1)
(2)
Divide by 8
Calculate
A
B
40gSin15 is NOT included as a moment about A. This is because it actually acts down the rod and through point A (as opposed to the place where it has been drawn), therefore it has a perpendicular distance of 0 and hence can be ignored…
7D

## Slide 35: Applications of Forces
15°
237
15°
40gSin15
You can solve problems about rigid bodies resting in limiting equilibrium
If a body is on the point of moving it is said to be in limiting equilibrium. In this case, the frictional force takes its maximum value, µR, where µ is the coefficient of friction and R is the normal reaction.
A uniform rod AB of mass 40kg and length 10m rests with the end A on rough horizontal ground. The rod rests against a smooth peg C where AC = 8m. The rod is in limiting equilibrium at an angle of 15° to the horizontal. Find:
The magnitude of the reaction at C
The coefficient of friction between the rod and the ground
15°
40g
40gCos15
R
F
A
B
Now you can resolve horizontally and vertically to find the remaining forces
You will need to split the normal reaction at the peg into horizontal and vertical components
The parallel and perpendicular components of the weight will no longer be needed…
237Cos15
237Sin15
Resolving Horizontally
Resolving Vertically
Rearrange
7D

## Slide 36: Applications of Forces
15°
237
You can solve problems about rigid bodies resting in limiting equilibrium
If a body is on the point of moving it is said to be in limiting equilibrium. In this case, the frictional force takes its maximum value, µR, where µ is the coefficient of friction and R is the normal reaction.
A uniform rod AB of mass 40kg and length 10m rests with the end A on rough horizontal ground. The rod rests against a smooth peg C where AC = 8m. The rod is in limiting equilibrium at an angle of 15° to the horizontal. Find:
The magnitude of the reaction at C
The coefficient of friction between the rod and the ground
15°
40g
R
F
A
B
As the rod is in limiting equilibrium, friction is at its maximum value
Use the formula for FMAX and sub in the values we have calculated
237Cos15
237Sin15
Sub in values
Divide by the bracket
Calculate
7D

## Slide 37: Applications of Forces
60°
60°
60°
2mg
You can solve problems about rigid bodies resting in limiting equilibrium
A ladder, AB, of mass m and length 3a, has one end A resting on rough horizontal ground. The other end, B, rests against a smooth vertical wall. A load of mass 2m is fixed on the ladder at point C, where AC = a. The ladder is modelled as a uniform rod and the load is modelled as a particle. The ladder rests in limiting equilibrium at an angle of 60° with the ground.
Find the coefficient of friction between the ladder and the ground.
A
B
C
RW
RG
F
mg
mgCos60
Start with a diagram and label all forces – both masses should be split into parallel and perpendicular components
We will now take moments about point A to give us the value of RW
60°
RWSin60
a
0.5a
1.5a
(1)
(2)
(3)
(1)
(2)
(3)
Cancel a’s
Group terms
Divide by 3Sin60
Calculate in terms of mg
2mgCos60
7D

## Slide 38: Applications of Forces
60°
60°
60°
2mg
You can solve problems about rigid bodies resting in limiting equilibrium
A ladder, AB, of mass m and length 3a, has one end A resting on rough horizontal ground. The other end, B, rests against a smooth vertical wall. A load of mass 2m is fixed on the ladder at point C, where AC = a. The ladder is modelled as a uniform rod and the load is modelled as a particle. The ladder rests in limiting equilibrium at an angle of 60° with the ground.
Find the coefficient of friction between the ladder and the ground.
A
B
C
RW
RG
F
mg
mgCos60
Now we can resolve horizontally and vertically
 This will allow us to find expressions for RG and F, and hence, the coefficient of friction
60°
RWSin60
a
0.5a
1.5a
(1)
(2)
(3)
2mgCos60
Resolving Horizontally
We already know RW so therefore also know F!
7D

## Slide 39: Applications of Forces
60°
60°
60°
2mg
You can solve problems about rigid bodies resting in limiting equilibrium
A ladder, AB, of mass m and length 3a, has one end A resting on rough horizontal ground. The other end, B, rests against a smooth vertical wall. A load of mass 2m is fixed on the ladder at point C, where AC = a. The ladder is modelled as a uniform rod and the load is modelled as a particle. The ladder rests in limiting equilibrium at an angle of 60° with the ground.
Find the coefficient of friction between the ladder and the ground.
A
B
C
RW
RG
F
mg
mgCos60
Now we can resolve horizontally and vertically
 This will allow us to find expressions for RG and F, and hence, the coefficient of friction
60°
RWSin60
a
0.5a
1.5a
(1)
(2)
(3)
2mgCos60
Resolving Vertically
Simplify
7D

## Slide 40: Applications of Forces
60°
60°
60°
2mg
You can solve problems about rigid bodies resting in limiting equilibrium
A ladder, AB, of mass m and length 3a, has one end A resting on rough horizontal ground. The other end, B, rests against a smooth vertical wall. A load of mass 2m is fixed on the ladder at point C, where AC = a. The ladder is modelled as a uniform rod and the load is modelled as a particle. The ladder rests in limiting equilibrium at an angle of 60° with the ground.
Find the coefficient of friction between the ladder and the ground.
A
B
C
RW
RG
F
mg
mgCos60
As the ladder is in limiting equilibrium, we can use the formula for friction
60°
RWSin60
a
0.5a
1.5a
(1)
(2)
(3)
2mgCos60
Sub in values
Cancel mg’s
Divide by 3
Calculate
7D

## Slide 41
Teachings for Exercise 7E

## Slide 42: Applications of Forces
You need to be able to solve problems involving dynamics on an inclined plane
A particle is held at rest on a rough plane inclined at an angle of θ to the horizontal, where Tanθ is 0.75. If the coefficient of friction between the particle and the plane is 0.5, find the acceleration of the particle.
You can find the below values (based on tanθ = 0.75) by drawing a right angled triangle and finding the hypotenuse (as in section 3D)
Tanθ = 3/4
Sinθ = 3/5 (0.6)
Cosθ = 4/5 (0.8)
θ
mkg
mg
θ
mgCosθ
mgSinθ
R
F
a
We need the normal reaction in order to find the maximum frictional force
 Resolve perpendicular to the plane
Resolve perpendicular to the plane
We have to use ‘m’ for now as we do not know the mass…
We know the value of Cosθ
0.8mg
0.8mg
7E

## Slide 43: Applications of Forces
You need to be able to solve problems involving dynamics on an inclined plane
A particle is held at rest on a rough plane inclined at an angle of θ to the horizontal, where Tanθ is 0.75. If the coefficient of friction between the particle and the plane is 0.5, find the acceleration of the particle.
You can find the below values (based on tanθ = 0.75) by drawing a right angled triangle and finding the hypotenuse (as in section 3D)
Tanθ = 3/4
Sinθ = 3/5 (0.6)
Cosθ = 4/5 (0.8)
θ
mkg
mg
θ
mgSinθ
F
a
Sub in values
Calculate
0.8mg
0.8mg
0.4mg
7E

## Slide 44: Applications of Forces
You need to be able to solve problems involving dynamics on an inclined plane
A particle is held at rest on a rough plane inclined at an angle of θ to the horizontal, where Tanθ is 0.75. If the coefficient of friction between the particle and the plane is 0.5, find the acceleration of the particle.
You can find the below values (based on tanθ = 0.75) by drawing a right angled triangle and finding the hypotenuse (as in section 3D)
Tanθ = 3/4
Sinθ = 3/5 (0.6)
Cosθ = 4/5 (0.8)
θ
mkg
mg
θ
mgSinθ
a
0.8mg
0.8mg
0.4mg
Now we have all the forces involved acting in the required directions, we can now calculate the acceleration of the particle…
 Resolve parallel to the plane
Sub in values and resolve parallel
The m’s cancel (meaning the mass does not affect the acceleration!)
Calculate a (remember, we know Sinθ)
7E

## Slide 45: Applications of Forces
You need to be able to solve problems involving dynamics on an inclined plane
A mass of 4kg is pushed up a plane by a horizontal force of magnitude 25N. The plane is inclined to the horizontal at 10° and the particle accelerates at 2.5ms-2. Calculate the coefficient of friction between the box and the plane.
In this type of question you should proceed as if you did have the coefficient of friction. You will end up with an equation where you can solve for µ.
10°
4kg
4g
10°
4gCos10
4gSin10
R
25N
10°
25Sin10
25Cos10
F
2.5ms-2
We need to split the forces into parallel and perpendicular components…
Now we can resolve perpendicular to find the normal reaction, and hence, the maximum frictional resistance created
Resolve perpendicular to the plane…
Sub in values and resolve perpendicular
Rearrange
Calculate
43N
7E

## Slide 46: Applications of Forces
You need to be able to solve problems involving dynamics on an inclined plane
A mass of 4kg is pushed up a plane by a horizontal force of magnitude 25N. The plane is inclined to the horizontal at 10° and the particle accelerates at 2.5ms-2. Calculate the coefficient of friction between the box and the plane.
In this type of question you should proceed as if you did have the coefficient of friction. You will end up with an equation where you can solve for µ.
10°
4kg
4g
10°
4gCos10
4gSin10
25N
10°
25Sin10
25Cos10
F
2.5ms-2
Now we can find the maximum frictional force created between the surfaces…
Sub in values (remember to use exact values, not rounded ones)
43N
Leave in terms of µ
43µ
7E

## Slide 47: Applications of Forces
You need to be able to solve problems involving dynamics on an inclined plane
A mass of 4kg is pushed up a plane by a horizontal force of magnitude 25N. The plane is inclined to the horizontal at 10° and the particle accelerates at 2.5ms-2. Calculate the coefficient of friction between the box and the plane.
In this type of question you should proceed as if you did have the coefficient of friction. You will end up with an equation where you can solve for µ.
10°
4kg
4g
10°
4gCos10
4gSin10
25N
10°
25Sin10
25Cos10
2.5ms-2
Now we have all the forces acting perpendicular to the plane, we can find the value of µ
43N
43µ
Resolve parallel to the plane…
Sub in values and resolve parallel
Rearrange to find µ
Solve exactly
Remember to use exact values!!
7E

## Slide 48
Teachings for Exercise 7F

## Slide 49: Section F – Connected Particles
You can solve problems involving connected particles on rough and smooth inclined surfaces

## Slide 50: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
Two particles, P and Q, of masses 5kg and 10kg are connected by a light inextensible string. The string passes over a small smooth pulley which is fixed at the top of a plane inclined at an angle of 25° to the horizontal. P is resting on the plane and Q hangs freely with the string vertical and taut. The coefficient of friction between P and the plane is 0.2.
Find the acceleration of the system
Find the tension in the string
25˚
25˚
5g
5gCos25
5gSin25
R
10g
P
Q
a
a
F
T
T
We will need to form 2 equations, one for each particle
For particle P, we need to calculate the frictional force first
Resolve perpendicular to find the normal reaction
Resolve perpendicular for P
Rearrange
5gCos25
Draw a diagram
 Remember to split the forces into parallel and perpendicular (where appropriate!)
7F

## Slide 51: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
Two particles, P and Q, of masses 5kg and 10kg are connected by a light inextensible string. The string passes over a small smooth pulley which is fixed at the top of a plane inclined at an angle of 25° to the horizontal. P is resting on the plane and Q hangs freely with the string vertical and taut. The coefficient of friction between P and the plane is 0.2.
Find the acceleration of the system
Find the tension in the string
25˚
25˚
5g
5gCos25
5gSin25
10g
P
Q
a
a
F
T
T
5gCos25
Draw a diagram
 Remember to split the forces into parallel and perpendicular (where appropriate!)
Sub in values for particle P
Calculate
gCos25
7F

## Slide 52: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
Two particles, P and Q, of masses 5kg and 10kg are connected by a light inextensible string. The string passes over a small smooth pulley which is fixed at the top of a plane inclined at an angle of 25° to the horizontal. P is resting on the plane and Q hangs freely with the string vertical and taut. The coefficient of friction between P and the plane is 0.2.
Find the acceleration of the system
Find the tension in the string
25˚
25˚
5g
5gCos25
5gSin25
10g
P
Q
a
a
T
T
5gCos25
Draw a diagram
 Remember to split the forces into parallel and perpendicular (where appropriate!)
gCos25
Now we can form 2 equations using P and Q
Equation for P
 Resolve Parallel
Equation for Q
 Resolve Vertically
Resolve Parallel for P
Resolve Vertically for Q
Solve for a
Add the equations together
 The T’s cancel out!
7F

## Slide 53: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
Two particles, P and Q, of masses 5kg and 10kg are connected by a light inextensible string. The string passes over a small smooth pulley which is fixed at the top of a plane inclined at an angle of 25° to the horizontal. P is resting on the plane and Q hangs freely with the string vertical and taut. The coefficient of friction between P and the plane is 0.2.
Find the acceleration of the system
Find the tension in the string
25˚
25˚
5g
5gCos25
5gSin25
10g
P
Q
a
a
T
T
5gCos25
Draw a diagram
 Remember to split the forces into parallel and perpendicular (where appropriate!)
gCos25
Use one of the previous equations to find the tension
We now know the acceleration
Solve for T
4.56ms-2
7F

## Slide 54: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
One end of a light inextensible string is attached to a block A of mass 2kg. The block A is held at rest on a smooth fixed plane which is inclined to the horizontal at an angle of 30˚. The string lies along the line of greatest slope of the plane (ie – up the plane), and passes over a smooth light pulley which is fixed at the top of the plane. The other end of the string is attached to a block B of mass 5kg. The system is released from rest. By modelling the blocks as particles and ignoring air resistance:
ai) Show that the acceleration of block B is
ii) Find the tension in the string
7F
30˚
30˚
2g
2gCos30
2gSin30
R
5g
A
B
a
a
T
T
Draw a diagram
 Remember to split the forces on the blocks into parallel and perpendicular (where appropriate!)
Note that as the plane is smooth, there will be no frictional force. Hence, we also do not need the normal reaction…
 Form equations for each block separately
Block A
Block B
Sub in values
Sub in values
Sin30 = 0.5

## Slide 55: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
One end of a light inextensible string is attached to a block A of mass 2kg. The block A is held at rest on a smooth fixed plane which is inclined to the horizontal at an angle of 30˚. The string lies along the line of greatest slope of the plane (ie – up the plane), and passes over a smooth light pulley which is fixed at the top of the plane. The other end of the string is attached to a block B of mass 5kg. The system is released from rest. By modelling the blocks as particles and ignoring air resistance:
ai) Show that the acceleration of block B is
ii) Find the tension in the string
7F
30˚
30˚
2g
2gCos30
2gSin30
R
5g
A
B
a
a
T
T
Draw a diagram
 Remember to split the forces on the blocks into parallel and perpendicular (where appropriate!)
 Add the equations together
Divide by 7
Sub this value in either 1) or 2) to get the tension…
1)
2)

## Slide 56: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
One end of a light inextensible string is attached to a block A of mass 2kg. The block A is held at rest on a smooth fixed plane which is inclined to the horizontal at an angle of 30˚. The string lies along the line of greatest slope of the plane (ie – up the plane), and passes over a smooth light pulley which is fixed at the top of the plane. The other end of the string is attached to a block B of mass 5kg. The system is released from rest. By modelling the blocks as particles and ignoring air resistance:
b) State how you have used the fact that the string is inextensible in your calculations
7F
30˚
30˚
2g
2gCos30
2gSin30
R
5g
A
B
a
a
T
T
Draw a diagram
 Remember to split the forces on the blocks into parallel and perpendicular (where appropriate!)
If the string is inextensible, it cannot stretch. Hence, the acceleration of both particles is the same
(you must remember to refer to your calculations, rather than just saying ‘the string doesn’t stretch…)

## Slide 57: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
One end of a light inextensible string is attached to a block A of mass 2kg. The block A is held at rest on a smooth fixed plane which is inclined to the horizontal at an angle of 30˚. The string lies along the line of greatest slope of the plane (ie – up the plane), and passes over a smooth light pulley which is fixed at the top of the plane. The other end of the string is attached to a block B of mass 5kg. The system is released from rest. By modelling the blocks as particles and ignoring air resistance:
c) Calculate the magnitude of the force exerted on the pulley by the string
7F
30˚
30˚
2g
2gCos30
2gSin30
R
5g
A
B
a
a
T
T
Draw a diagram
 Remember to split the forces on the blocks into parallel and perpendicular (where appropriate!)
60˚
30˚
30˚
The force on the pulley comes from the tension in the string in both directions
 Since the Tensions are equal, the resultant force will be along the angle bisector for the angle at the top of the plane
 You can split each Tension into components parallel to the resultant force and perpendicular to it

## Slide 58: Applications of Forces
You can solve problems involving connected particles on rough and smooth inclined surfaces
One end of a light inextensible string is attached to a block A of mass 2kg. The block A is held at rest on a smooth fixed plane which is inclined to the horizontal at an angle of 30˚. The string lies along the line of greatest slope of the plane (ie – up the plane), and passes over a smooth light pulley which is fixed at the top of the plane. The other end of the string is attached to a block B of mass 5kg. The system is released from rest. By modelling the blocks as particles and ignoring air resistance:
c) Calculate the magnitude of the force exerted on the pulley by the string
7F
30˚
30˚
2g
2gCos30
2gSin30
R
5g
A
B
a
a
T
T
Draw a diagram
 Remember to split the forces on the blocks into parallel and perpendicular (where appropriate!)
60˚
30˚
30˚
So the overall resultant force on the pulley will equal:
We know the value of
Simplify